## Slide 1: Highlight Reel: Slide Decks 3.0 – 5.0 ENGR-E 399/599: VLSI Design Prof. Daniel Loveless, dlovele@iu.edu, 812-856-0703
INDIANA UNIVERSITY – Reliable Electronics and Systems
Center for Reliable and Trusted Electronics (CREATE)
Notes: Hello and welcome. Today, our focus will be on the CMOS transistor theory.

## Slide 2: nMOS Linear I-V
Now we know
  How much charge Qchannel is in the channel
  How much time (t) each carrier takes to cross
Vgs > Vt
But Vds small
Channel forms
Current flows from d to s
  e- from s to d
Ids increases with Vds
Similar to linear resistor

## Slide 3: nMOS Saturation I-V
If Vgd < Vt, channel pinches off near drain
  When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current
Vgs > Vt
Vds > Vgs - Vt
Channel pinches off
Ids independent of Vds
We say current saturates
Similar to current source

## Slide 4: I-V Summary
Shockley 1st order transistor models
nMOS
pMOS
Notes: The equation for Ids current can be expressed for the three operating regions cutoff, linear and saturation.

## Slide 5: Non-Ideal Transistors
Non-ideal effects include:
  Short channel effect
  Leakage:
    Subthreshold conduction
    Gate
    Junction
  Temperature sensitivity
  Parameter variation
Notes: Plot shows Simulated vs Ideal I-V characteristics of the nMOS transistor. This plot highlights the difference between the ideal and non-ideal transistor. In the plot, it can be seen that the velocity saturation and mobility degradation for the simulated model is lower than that of the ideal transistor.

## Slide 6: Operation
Region | nMOS | pMOS
A | Cutoff | Linear
B | Saturation | Linear
C | Saturation | Saturation
D | Linear | Saturation
E | Linear | Cutoff
Notes: Plot shows Simulated vs Ideal I-V characteristics of the nMOS transistor. This plot highlights the difference between the ideal and non-ideal transistor. In the plot, it can be seen that the velocity saturation and mobility degradation for the simulated model is lower than that of the ideal transistor.

## Slide 7: Matching
Notes: Plot shows Simulated vs Ideal I-V characteristics of the nMOS transistor. This plot highlights the difference between the ideal and non-ideal transistor. In the plot, it can be seen that the velocity saturation and mobility degradation for the simulated model is lower than that of the ideal transistor.

## Slide 8: Inverter Step Response
E.g., find step response of inverter driving load cap

## Slide 9: Delay Definitions
tpdr: rising propagation delay
  From input to rising output crossing VDD/2
tpdf: falling propagation delay
  From input to falling output crossing VDD/2
tpd: average propagation delay
  tpd = (tpdr + tpdf)/2
tr: rise time
  From output crossing 0.2 VDD to 0.8 VDD
tf: fall time
  From output crossing 0.8 VDD to 0.2 VDD

## Slide 10: Delay Definitions
tcdr: rising contamination delay
  From input to rising output crossing VDD/2
tcdf: falling contamination delay
  From input to falling output crossing VDD/2
tcd: average contamination delay
  tpd = (tcdr + tcdf)/2
Notes: Contamination delay is the minimum time from when the input changes to 50% of its value to when the output changes to 50% of its value.

## Slide 11: Delay Estimation
We would like to be able to easily estimate delay
  Not as accurate as simulation
  But easier to ask “What if?”
The step response usually looks like a 1st order RC response with a decaying exponential.
Use RC delay models to estimate delay
  C = total capacitance on output node
  Use effective resistance R
  So that tpd = RC
Characterize transistors by finding their effective R
  Depends on average current as gate switches
Notes: Step response use RC delay models to estimate delay.
C=strain capacitance and R is the equivalent resistance of the transistors, depending on its average current.

## Slide 12: Effective Resistance
Shockley models have limited value
  Not accurate enough for modern transistors
  Too complicated for much hand analysis
Simplification: treat transistor as resistor
  Replace Ids(Vds, Vgs) with effective resistance R
    Ids = Vds/R
  R averaged across switching of digital gate
Too inaccurate to predict current at any given time
  But good enough to predict RC delay
Notes: To find the effective resistance of a transistor, the Shockley model can be used, however this model is limited because it is not suitable for modern transistors.
The designer can treat the transistor as a resistor. This approach is good enough to predict RC delay of the transistor.

## Slide 13: RC Delay Model
Use equivalent circuits for MOS transistors
  Ideal switch + capacitance and ON resistance
  Unit nMOS has resistance R, capacitance C
  Unit pMOS has resistance 2R, capacitance C
Capacitance proportional to width
Resistance inversely proportional to width
Notes: Here, we have some guidelines to transform transistors into equivalent circuits.
Treat the transistor as an ideal switch with Resistance (in on condition) and Capacitance (all connected to 0V/Vdd).
nMOS has resistance R (between the gate to source) divided by the constant of the transistor and capacitance C (connected to Vdd) multiplied by the constant of the transistor.
pMOS has resistance 2R (between the gate to the drain) divided by the constant of the transistor and capacitance C (connected to 0 V) multiplied by the constant of the transistor.

## Slide 14: RC Values
Capacitance
  C = Cg = Cs = Cd = 2 fF/mm of gate width in 0.6 mm
  Gradually decline to 1 fF/mm in nanometer techs.
Resistance
  R ≈ 6 kΩ*mm in 0.6 mm process
  Reduces with shorter channel lengths
Unit transistors
  May refer to minimum contacted device (4/2 l)
  Or maybe 1 mm wide device
  Doesn’t matter as long as you are consistent

## Slide 15: Inverter Delay Estimate
Estimate the delay of a fanout-of-1 inverter
Notes: First, transform the transistors into the ideal switch with resistances and capacitances.
Next consider only the active network based on the input value. The delay through the active network can be calculated by multiplying the total resistance (R) with the total capacitance (6C because capacitances are in parallel).
tpd=6RC.

## Slide 16: Delay Model Comparison

## Slide 17: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R).
Notes: Example of a 3-input NAND gate with gate sizing to achieve effective rise and fall resistance equal to a unit inverter.
All the pMOS have constant k=2 and all the nMOS have constant k=3.

## Slide 18: 3-input NAND Caps
Annotate the 3-input NAND gate with gate and diffusion capacitance.

## Slide 19: Elmore Delay
ON transistors look like resistors
Pullup or pulldown network modeled as RC ladder
Elmore delay of RC ladder
Notes: Elmore Delay: It is usually used for tree-structured networks where the formula is similar to the tpd where it is the sum of RC.
Pullup and Pulldown network can be modeled as RC ladders.
We can use this theory to continue working with the 3 input NAND CAPS and calculate the equivalent delay.

## Slide 20: Example: 3-input NAND
Estimate worst-case rising and falling delay of 3-input NAND driving h identical gates.
Notes: Draw the RC equivalent of the transistors to estimate the rising and falling delay.

## Slide 21: Delay Components
Delay has two parts
  Parasitic delay
    9 or 11 RC
    Independent of load
  Effort delay
    5h RC
    Proportional to load capacitance
Notes: Delay in gates have two components:
Parasitic delay. This is independent of the load as shown in previous examples modeling the RC equivalent of the transistors.
The effort delay is mainly or directly proportional to the load capacitance.

## Slide 22: Contamination Delay
Best-case (contamination) delay can be substantially less than propagation delay.
E.g., if all three inputs fall simultaneously

## Slide 23: Diffusion Capacitance
We assumed contacted diffusion on every s/d.
Good layout minimizes diffusion area
E.g., NAND3 layout shares one diffusion contact
  Reduces output capacitance by 2C
  Merged uncontacted diffusion might help too
Notes: It is possible for transistor to share diffusion area to minimize diffusion capacitance. This is an optimization of the layout.

## Slide 24: Layout Comparison
Which layout is better?
Left has less diffusion capacitance on Y