## Slide 1: EXAMPLE Critical Design Review (CDR)
Prof. Daniel Loveless
4/22/2025

## Slide 2: Executive Summary
Problem: Random-telegraph-signal (RTS) noise is a known detractor for Focal Plane Array / Read-Out IC (ROIC) designs
Solution: Minimize RTS noise contributors in a commercial 90 nm bulk CMOS technology (C90)
Objective / Goal: Identify root cause(s) / contributors of RTS noise (through 3 process revisions, DOE-1/2/3) and develop appropriate responses to minimize or eliminate the adverse effects of these contributors in C90
This critical design review (CDR) for DOE-3 documents the proposed changes to existing test structures to fix known issues with DOE-1 and DOE-2 and for improvement of measurement capabilities.
UNCLASSIFIED//FOUO

## Slide 3: DOE-3 Objectives
DOE-1 Objectives:
  Framework for large-scale RTS characterization of active C90 devices
  Eight primary transistor types implemented with various aspect ratios
DOE-2 Objectives:
  Improvement/upgrade of RTS measurement approach; RTS benchmarking
  Demonstration of RTS in ROIC sub-circuits
  Characterize baseline sensitivity of C90 process to ionizing radiation
DOE-3 Objectives:
  Fix the known issue with DOE-1 pMOS array
  Fix known issue with DOE-2 DICE shift register
  Include annular gate transistor arrays for RTS and radiation effects evaluation
UNCLASSIFIED//FOUO

## Slide 4: Anticipated Timeline
CDR (date)
GDS Submission (date)
Tapeout (date)
SEE Rad testing of DOE-2 (date)
DOE-3 Packaging (date)
RTS and Radiation testing of DOE-3 begins (date)
UNCLASSIFIED//FOUO

## Slide 5: DOE-1, DOE-2, DOE-3 Designs
DOE-1
RadFX
    Built-in-self-test for:
      RTS capture
      Source followers
      Issue with pMOS array in Chiplet 1
DOE-2
CTIA
    Built-in-self-test for:
      RTS capture
      CTIA
      No known issues
    Built-in-self-test for:
      Radiation Characterization
      Known issue with DICE shift reg.
DOE-3
    DOE-1-v3
      Fixed issue with pMOS source follower array
      Added high-voltage annular structures to Probe Array (Chiplet 2)
    DOE-2-CTIA-v3
      No changes
    DOE-2-RADFX-v3
      Repaired issue with DICE
UNCLASSIFIED//FOUO

## Slide 6: DOE-3 (DOE-1-v3)
Two 2.3 mm x 2.1 mm
One 4.6 mm x 2.1 mm
Chiplet 1 (24 x 24 probe pads)
  Transistor array to include:
SC and BC devices
W/L variants
Thick and thin oxide variants
Bulk (p-substrate) and deep n-well
Chiplet 1A (24 x 24 probe pads)
  Transistor arrays to include HV annular devices
Chiplet 3 (78 bond pads)
  On-chip RTS transistor array with repaired pMOS
4.430 mm x 4.945 mm
Divided into 3 chiplets
Chiplet 3
Chiplet 1A
Chiplet 1
UNCLASSIFIED//FOUO

## Slide 7: DOE-3 Chiplet 1 RTS Source Follower Array
UNCLASSIFIED//FOUO

## Slide 8: DOE-1-v3 On-Chip RTS Structures
On-chip RTS measurement uses a built-in-self-test (BIST) architecture for testing of a large transistor array (~2x104 transistors – 256x96)
Transistors configured as source- follower amplifiers with on-chip current source bias
Analog array with 8 channels
Packaged in a 100-pin LCC
Bond pad pitch is 140 𝝁m (70 𝝁m x 70 𝝁m pad size)
I/O cells with electro-static discharge (ESD) protection
UNCLASSIFIED//FOUO

## Slide 9: DOE-1-v3 On-Chip RTS Structures
GS
RTS manifests as discrete shifts in V
Capture (𝞃C) and emission (𝞃E) time constants will be measured
A typical measurement:
  ~60 sec (2KHz bandwidth)
  Bias setup: 20 sec
  DC measurement: 2 ~ 5 sec
  RTS Sampling: 20 sec
The device under test (DUT) within each Unit Cell will be biased as a source follower using an on-chip current source (IDS) and an externally applied gate bias (VG)
ΔVS is measured via an on-chip amplifier, thus allowing for extraction of ΔVGS
IREF
Unit Cell
VG
I
DS
RS(j)
CS(i)
VN
VP BH
VOUT
ΔVS
Vgs = VG-VOUT
UNCLASSIFIED//FOUO

## Slide 10: DOE1 NMOS Current Source
NMOS is correct
IBIAS is connected to the first cascaded MOS
UNCLASSIFIED//FOUO

## Slide 11: DOE1_v3 PMOS Array Fix
PMOS cell correct, however, the external reference pin was connected to the wrong node
IBIAS was connected to the second cascaded MOS
UNCLASSIFIED//FOUO

## Slide 12: DOE1_v3 PMOS Array Fix
PMOS is correct
IBIAS is connected to the first cascaded MOS
UNCLASSIFIED//FOUO

## Slide 13: DOE1_v3 PMOS Array Fix - Layout
UNCLASSIFIED//FOUO

## Slide 14: DOE1_v3 PMOS Array Fix - LVS
UNCLASSIFIED//FOUO

## Slide 15: DOE-3 RADFX
UNCLASSIFIED//FOUO

## Slide 16: DOE-2/3 Radiation Effects Test Coupon (RADFX)
Single-event transients (SET)
  SETs are a fundamental circuit-level response critical for model calibration
  Large targets of combinational logic (INV, NAND, OR) will be used to generate SETs (with expected pulse widths between 50 ps and 1 ns) captured by an on-chip time-to-digital converter (TDC)
Single-event upsets (SEU)
  Single-event effects that result in a change in the state of memory
  Shift registers designed from Skywater standard cell flip-flops and a radiation-hardened cell will be used to determine the critical charge to upset
  Shift registers will be laid out with varying well/substrate contact densities to characterize critical charge versus tap spacing
Single-event latchup (SEL)
  Potentially destructive response to single-event effects due to coupled parasitic bipolar devices
  The entire test article will be used to screen the process and the shift registers (with varying contact densities) used to characterize if necessary
Total-Ionizing Dose (TID)
  Transistor test arrays (bonded or probed) used to characterize shifts in threshold voltage and leakage current
  On-chip ring-oscillators used to measure shifts in drive current
UNCLASSIFIED//FOUO

## Slide 17: DOE-2/3 Radiation Effects Test Coupon (RADFX)
Single-event transients (SET)
  SETs are a fundamental circuit-level response critical for model calibration
  Large targets of combinational logic (INV, NAND, OR) will be used to generate SETs (with expected pulse widths between 50 ps and 1 ns) captured by an on-chip time-to-digital converter (TDC)
Single-event upsets (SEU)
  Single-event effects that result in a change in the state of memory
  Shift registers designed from Skywater standard cell flip-flops and a radiation-hardened cell will be used to determine the critical charge to upset
  Shift registers will be laid out with varying well/substrate contact densities to characterize critical charge versus tap spacing
Single-event latchup (SEL)
  Potentially destructive response to single-event effects due to coupled parasitic bipolar devices
  The entire test article will be used to screen the process and the shift registers (with varying contact densities) used to characterize if necessary
Total-Ionizing Dose (TID)
  Transistor test arrays (bonded or probed) used to characterize shifts in threshold voltage and leakage current
  On-chip ring-oscillators used to measure shifts in drive current
UNCLASSIFIED//FOUO
The dual-interlocked cell (DICE) on DOE-2-RADFX has some timing issues – this will be corrected in DOE-3

## Slide 18: Shift Registers (SREG) – H Clocking Method
UNCLASSIFIED//FOUO

## Slide 19: Shift Registers (SREG) – H Clocking Method
UNCLASSIFIED//FOUO

## Slide 20: Shift Registers (SREG) – H Clocking Method
UNCLASSIFIED//FOUO

## Slide 21: Shift Registers (SREG) – H Clocking Method
UNCLASSIFIED//FOUO

## Slide 22: Shift Registers (SREG) – H Clocking Method
UNCLASSIFIED//FOUO

## Slide 23: DICE Schematic
UNCLASSIFIED//FOUO

## Slide 24: DICE Layout
UNCLASSIFIED//FOUO

## Slide 25: DICE Shift Register Layout
1x 2x 3x 4x
5x 6x 7x 8x
UNCLASSIFIED//FOUO

## Slide 26: DICE 1024x Shift Register
Design Choice: H-Tree clocking
Why: All flip-flops are clocked simultaneously
UNCLASSIFIED//FOUO

## Slide 27: DICE Size Increase → 32.47%
UNCLASSIFIED//FOUO

## Slide 28: DICE Functionality
Frequency: 2 GHz
Pulse Width: 50 ps
UNCLASSIFIED//FOUO

## Slide 29: DICE - LVS
UNCLASSIFIED//FOUO

## Slide 30: DRC Rule Waivers Needed
UNCLASSIFIED//FOUO

## Slide 31: Summary
This critical design review (CDR) for DOE-3 documents the proposed changes to existing test structures to fix known issues with DOE-1 and DOE-2 and for improvement of measurement capabilities.
All designs are 100% complete
The final pattern density fill is currently being synthesized
GDS files will be delivered to manufacturer by <date>
UNCLASSIFIED//FOUO
DOE-3
    DOE-1-v3
      Fixed issue with pMOS source follower array
      Added high-voltage annular structures to Probe Array (Chiplet 2)
    DOE-2-CTIA-v3
      No changes
    DOE-2-RADFX-v3
      Repaired issue with DICE